## Slide 1
The inherited tank-fill workbook
1 / 8
Renato Jacinto · EGN 321 · Assignment 8.2
Original input | R-101, Tank Fill row 6
Length and width | 10 ft × 6 ft
Fill depth | 8 in = 0.666667 ft
Calculated volume | 40 ft³ = 299.2208 US gal
Original artifact: TANK_FILL_rev4.xlsx
Notes: 0:00–0:55. My project began with TANK_FILL_rev4.xlsx, an inherited production fill log. The workbook takes tank length and width in feet and a depth labeled in inches, then outputs US gallons. It includes 18 runs and separate field notes. Open the actual original workbook to show Tank Fill row 6, where R-101 has length 10 feet, width 6 feet, and depth 8 inches. Explain that this is a rectangular tank calculation. Converting depth to feet first gives 40 cubic feet. Multiplying by the inherited conversion convention gives 299.2208 US gallons. The original artifact is included unchanged in the submission. Source: original/TANK_FILL_rev4.xlsx, Tank Fill!C6:G6.

## Slide 2
The workbook risks
2 / 8
Finding | Engineering consequence
R-108: 2.5 ft recorded as 2.5 in | 93.5065 versus 1122.0780 US gal
G25 sums G6:G17 | Six of the 18 runs are omitted
Conversion literals repeat in formulas | Units and assumptions are harder to audit
Explicit depth units, named constants, and complete case comparisons
Notes: 0:55–1:50. The formula works for known-correct inputs, but input meaning and total coverage require review. Show Tank Fill E13 and Field Notes E11 for R-108. The field note says 2.5 feet while the formula treats the entered 2.5 as inches. That produces a twelvefold difference. Also show G25: its formula sums only G6:G17, excluding the last six runs. Explain that matching an existing number does not prove that its units or total range are right. The new code names its conversion constants and the interface makes the depth unit explicit. The verification report retains both interpretations of the source discrepancy. Source: WORKBOOK_VERIFICATION.md and the original workbook.

## Slide 3
Capabilities in the final delivery
3 / 8
Course topic | Final evidence
Defects, units, reusable logic | Workbook comparison and tank_fill.py
Interface and simulated input | Tank form and sensor CSV replay
History and unattended operation | SQLite, dashboard, alerts, supervisor
Operation and final delivery | Guide, improvements, tests, presentation
Final capability map. Historical commits are not reconstructed.
Notes: 1:50–2:40. The course added capabilities in stages: checking inherited assumptions, validating units, separating reusable functions, building interfaces, replaying sensor input, preserving history, and monitoring health and recovery. The final package combines the saved Module 7 monitor with a tank calculation page added for the final delivery. This table maps capabilities to final files. It does not establish an exact historical commit sequence. The sensor dataset is the later Module 6 classroom file with five channels. Temperature is not a tank-depth measurement, so the system keeps the workflows separate. Source: CAPSTONE_REPORT.md, tank_fill.py, history.py, app.py.

## Slide 4
Final application architecture
4 / 8
Tank calculation
Form inputs with explicit units
Reusable geometry calculation
ft³ and US gallon result
Calculation or refusal log
Sensor monitoring
CSV replay and validation
SQLite archive and replay history
Health, alerts, and dashboard
Supervisor restart and logs
Temperature does not supply tank depth. Both workflows share the Flask app.
Notes: 2:40–3:25. Explain the two workflows. The tank form passes its dimensions and explicit depth unit into tank_fill.calculate, which validates values and returns cubic feet and gallons. The sensor worker validates source readings, writes archive and replay records in SQLite, updates alert state, and supplies the dashboard. Both workflows write events to the application log. supervisor.py runs the monitoring process and restarts it after an unexpected child exit. Explain that the tank calculator remains usable even though temperature monitoring has its own health state. Source: app.py, tank_fill.py, alert_logic.py, supervisor.py.

## Slide 5
Live demonstration
5 / 8
Action | Expected behavior
10 ft × 6 ft × 8 in | 299.2208 US gal
10 ft × 6 ft × 2.5 ft | 1122.0780 US gal
Depth = −1 | Calculation refused with a reason
Open dashboard and history | Replay status and original timestamps
http://127.0.0.1:5000/tank
Notes: 3:25–5:10. Switch to the running application. Open /tank. Submit 10 feet by 6 feet with 8 inches depth and show 299.2208 US gallons. Compare the result with workbook G6. Next enter depth 2.5 and explicitly choose feet. Show 1122.0780 US gallons and explain the R-108 difference. Enter depth minus one and show the clear refusal. Refusing an impossible depth is better than returning a plausible-looking negative volume. Restore valid input. Open the sensor dashboard and history page. Explain original source time versus today's replay receipt time. The receipt timestamp indicates replay activity and does not turn historical data into a new physical measurement. Source: LIVE_DEMO.md and the live local application.

## Slide 6
Calculation and test evidence
6 / 8
21 passing test cases
Required case | Verification
Known-correct workbook case | R-101 matches 299.2208 US gal
Problem / edge case | R-108 unit regression and omitted total
Invalid input | HTTP 400 and specific refusal message
Additional domain case | Zero depth returns zero volume
All 18 original cached row values match the entered-inch calculations.
Notes: 5:10–6:10. Show the 21 passing test cases in the terminal and the workbook comparison report. The known-correct case anchors the new calculation to the original artifact. The R-108 regression checks the unit discrepancy. Invalid input cases include negative, missing, nonfinite, zero dimensions, unsupported units, and overflow. The additional domain test checks zero depth as a valid empty tank. This test was prepared with AI assistance and needs my own explanation. All 18 cached workbook row results agree when interpreted as entered inches. The full totals are reported separately from the incomplete legacy total. Source: tests/test_tank_fill.py, tests/test_monitor.py, evidence/workbook_verification.json.

## Slide 7
Failure, recovery, and operation
7 / 8
Controlled fault
Pause replay to expose STALE and FAILED.
Kill the application child to test automatic restart.
Recovery evidence
Changed PID, resumed HTTP service, HEALTHY state
8,780 archive records retained, SQLite integrity = ok
Optional partner observation omitted. Setup and recovery instructions improved through review.
Notes: 6:10–7:45. Run the separate controlled-failure script if time permits, or open its actual saved evidence. It first shows healthy input, high-temperature alert activation and clearing, then paused delivery becoming stale and failed. It also verifies missing input. It then kills the child process and verifies the new PID, responding HTTP service, resumed healthy status, retained records, and database integrity. Show those fields in evidence/verification.json and the corresponding log entries. Explain that these are synthetic classroom fault inputs at a 0.5-second delivery interval in the assistant Linux environment. The optional silent partner observation was omitted based on the instructor clarification reported by the student. Documentation improvements came from source and workflow review, so no partner struggle is claimed. Source: VERIFICATION_REPORT.md, evidence/verification.json, IMPROVEMENTS.md.

## Slide 8
Limits and lessons
8 / 8
Rectangular geometry and explicit units define the calculation.
Tank capacity and physical calibration remain unverified.
Finite replay and surviving storage limit recovery.
A result needs a traceable input, a test, and a stated boundary.
AI assistance is recorded in AI_LOG.md.
The live code challenge and defense must be completed without AI.
Notes: 7:45–8:40. Close with the limits. The tank calculation assumes a level rectangular tank with vertical walls. It does not know the tank's maximum height, so a valid calculated volume does not prove that a fill is safe. Monitoring cannot verify physical calibration, and the replay is finite. Automatic restart requires the supervisor and storage to survive. The operating guide now gives exact commands, explicit units, and evidence paths so another operator can follow it. AI helped during development and preparation, and the specific assistance is recorded in AI_LOG.md. I must understand the final code and complete the instructor's live modification and questions independently, without AI. Source: README.md, CODE_DEFENSE.md, AI_LOG.md.